## Slide 1: Physical Security

## Slide 2: Learning Objectives
Upon completion of this material, you should be able to:
  Discuss the relationship between information security and physical security
  Describe key physical security considerations, including fire control and surveillance systems
  Identify critical physical environment considerations for computing facilities, including uninterruptible power supplies
Notes: Upon completion of this material you should be able to:
Understand the conceptual need for physical security
Identify threats to information security that are unique to physical security
Describe the key physical security considerations for selecting a facility site
Identify physical security monitoring components
Grasp the essential elements of access control within the scope of facilities management
Understand the criticality of fire safety programs to all physical security programs
Describe the components of fire detection and response
Grasp the impact of interruptions in the service of supporting utilities
Understand the technical details of uninterruptible power supplies and how they are used to increase availability of information assets
Discuss critical physical environment considerations for computing facilities
Discuss countermeasures to the physical theft of computing devices

## Slide 3: Introduction
Physical security addresses design, implementation, and maintenance of countermeasures that protect physical resources of an organization
Most controls can be circumvented if an attacker gains physical access
Physical security is as important as logical security
Notes: Introduction
Physical security addresses design, implementation, and maintenance of countermeasures that protect the physical resources of an organization.
Most of the technology-based controls discussed to this point can be circumvented if an attacker gains physical access to the devices being controlled.
Some computer systems are constructed in such a way that it is easy to steal the hard drive and the information it contains.
As a result, physical security should receive as much attention as logical security in the security development life cycle.

## Slide 4: Introduction (cont’d.)
Seven major sources of physical loss:
  Extreme temperature
  Gases
  Liquids
  Living organisms
  Projectiles
  Movement
  Energy anomalies
Notes: Seven Major Sources of Physical Loss
From Donn B. Parker
Extreme temperature: heat, cold
Gases: war gases, commercial vapors, humid or dry air, suspended particles
Liquids: water, chemicals
Living organisms: viruses, bacteria, people, animals, insects
Projectiles: tangible objects in motion, powered objects
Movement: collapse, shearing, shaking, vibration, liquefaction, flows waves, separation, slide
Energy anomalies: electrical surge or failure, magnetism, static electricity, aging circuitry; radiation: sound, light, radio, microwave, electromagnetic, atomic

## Slide 5: Introduction (cont’d.)
Community roles
  General management: responsible for facility security
  IT management and professionals: responsible for environmental and access security
  Information security management and professionals: perform risk assessments and implementation reviews
Notes: Community Roles
General management: responsible for the security of the facility in which the organization is housed and the policies and standards for secure operation
IT management and professionals: responsible for environmental and access security in technology equipment locations and for the policies and standards of secure equipment operation
Information security management and professionals: perform risk assessments and implementation reviews for the physical security controls implemented by the other two groups

## Slide 6: Physical Access Controls
Secure facility: physical location engineered with controls designed to minimize risk of attacks from physical threats
Secure facility can take advantage of natural terrain, traffic flow, and degree of urban development; can complement these with protection mechanisms (fences, gates, walls, guards, alarms)
Notes: Facilities Management
Before examining access controls, understand the concept of a secure facility and its design.
From the point of view of facilities management, a secure facility is a physical location that has been engineered with controls designed to minimize the risk of attacks from physical threats.
A secure facility can use the natural terrain, traffic flow, and urban development, and can complement these features with protection mechanisms such as fences, gates, walls, guards, and alarms.

## Slide 7: Physical Security Controls
Walls, fencing, and gates
Guards
Dogs
ID cards and badges
Locks and keys
Mantraps
Electronic monitoring
Alarms and alarm systems
Computer rooms and wiring closets
Interior walls and doors
Notes: Controls for Protecting the Secure Facility
There are a number of physical security controls and issues that the organization’s communities of interest should consider together when implementing physical security:
Walls, fencing, and gates
Guards to apply human reasoning
Dogs to provide their keen sense of smell and hearing and to be placed in harm’s way in lieu of humans
ID cards and badges
Locks and keys
Mantraps
Electronic monitoring
Alarms and alarm systems
Computer rooms
Walls and doors

## Slide 8: Physical Security Controls (cont’d.)
ID Cards and Badges
  Ties physical security with information access control
    ID card is typically concealed
    Name badge is visible
  Serve as simple form of biometrics (facial recognition)
  Should not be only means of control as cards can be easily duplicated, stolen, and modified
  Tailgating occurs when unauthorized individual follows authorized user through the control
Notes: ID Cards and Badges
One area of access control that ties physical security with information access control is the use of identification cards (ID) and name badges. An ID card is typically worn concealed, whereas a name badge is visible.
These devices are forms of biometrics (facial recognition) to identify and authenticate an authorized individual with access to the facility.
With the addition of a magnetic strip or radio chip, the ID card can provide access control.
A name badge or ID should not be the only control for access to restricted areas, as they can be easily duplicated, stolen, and modified.
Tailgating occurs when an authorized individual presents a key and a door is opened, but other individuals, who may or may not be authorized, also enter the unlocked door.

## Slide 9: Physical Security Controls (cont’d.)
Locks and keys
  Two types of locks: mechanical and electromechanical
  Locks can also be divided into four categories: manual, programmable, electronic, biometric
  Locks fail and alternative procedures for controlling access must be put in place
  Locks fail in one of two ways:
    Fail-safe lock
    Fail-secure lock
Notes: Locks and Keys
There are two types of locks: mechanical and electromechanical.
The mechanical lock relies on a key of carefully shaped pieces of metal that turn tumblers to release secured loops of steel, aluminum, or brass (in brass padlocks).
The electromechanical lock can accept a variety of inputs including keys that are magnetic strips on ID cards, radio signals from name badges, PINs typed into a keypad.
Locks are divided into four categories: manual, programmable, electronic, and biometric.
As part of general management’s responsibility for the physical environment, the management of keys and locks is a fundamental concern.
Sometimes locks fail and facilities need alternative procedures for access.
Locks fail in one of two ways: when the lock of a door fails and the door becomes unlocked, that is a fail-safe lock; when the lock of a door fails and the door remains locked, this is a fail-secure lock.

## Slide 10
Figure 9-1 Locks

## Slide 11: Physical Security Controls (cont’d.)
Mantrap
  Small enclosure that has entry point and different exit point
  Individual enters mantrap, requests access, and if verified, is allowed to exit mantrap into facility
  Individual denied entry is not allowed to exit until security official overrides automatic locks of the enclosure
Notes: Mantraps
A mantrap is a small enclosure that has an entry point and a different exit point.
The individual entering the facility, area, or room, enters the mantrap, requests access through some form of electronic or biometric lock and key, and if verified, is allowed to exit the mantrap into the facility.
This is called a mantrap, because if the individual is denied entry, the mantrap does not allow exit until a security official overrides the automatic locks of the enclosure.

## Slide 12
Figure 9-2 Mantraps

## Slide 13: Physical Security Controls (cont’d.)
Electronic Monitoring
  Records events where other types of physical controls are impractical or incomplete
  May use cameras with video recorders; includes closed-circuit television (CCT) systems
  Drawbacks
    Reactive; does not prevent access or prohibited activity
    Recordings often are not monitored in real time; must be reviewed to have any value
Notes: Electronic Monitoring
Used to record events within a specific area or areas where other types of physical controls are not practical.
Monitoring frequently uses cameras viewing individuals, while on the other end of these cameras are video cassette recorders and related machinery that captures the video feed.
These systems have drawbacks, as for the most part they are reactive and do not prevent access or prohibited activity.
Recorded monitoring requires an individual to review the information collected.

## Slide 14: Physical Security Controls (cont’d.)
Alarms and alarm systems
  Alarm systems notify when an event occurs
  Detect fire, intrusion, environmental disturbance, or an interruption in services
  Rely on sensors that detect event; e.g., motion detectors, smoke detectors, thermal detectors, glass breakage detectors, weight sensors, contact sensors, vibration sensors
Notes: Alarms and Alarm Systems
Alarm systems notify appropriate individuals when a predetermined event or activity occurs.
This could be a fire, a break-in or intrusion, an environmental disturbance, such as flooding, or an interruption in services, such as a loss of power.
Burglar alarm systems detect intrusions into unauthorized areas and notify either a local or remote security agency to react.
These systems rely on a number of sensors that detect the intrusion: motion detectors, thermal detectors, glass breakage detectors, weight sensors, and contact sensors.

## Slide 15: Physical Security Controls (cont’d.)
Computer rooms and wiring closets
  Require special attention to ensure confidentiality, integrity, and availability of information
  Logical controls easily defeated if attacker gains physical access to computing equipment
  Custodial staff often the least scrutinized persons who have access to offices; are given greatest degree of unsupervised access
Notes: Computer Rooms and Wiring Closets
Computer rooms and wiring and communications closets are facilities that require special attention to ensure the confidentiality, integrity, and availability of information.
Logical access controls are easily defeated if an attacker gains physical access to the computing equipment.
Custodial staff are often the least scrutinized of employees and nonemployees who have access to offices. Yet custodians are given the greatest degree of unsupervised access.

## Slide 16: Physical Security Controls (cont’d.)
Interior walls and doors
  Information asset security sometimes compromised by construction of facility walls and doors
  Facility walls typically either standard interior or firewall
  High-security areas must have firewall-grade walls to provide physical security from potential intruders and improve resistance to fires
  Doors allowing access to high security rooms should be evaluated
  Recommended that push or crash bars be installed on computer rooms and closets
Notes: Interior Walls and Doors
The security of information assets can sometimes be compromised because of the construction of the walls and doors of the facility.
The walls in a facility are typically: standard interior or firewall.
All high-security areas, such as computer rooms and wiring closets, must have firewall-grade walls surrounding them.
This provides not only physical security from potential intruders but from fires as well.
The doors that allow access into these types of secured rooms should also be evaluated.
Computer rooms and wiring closets can have push or crash bars installed.
Such devices meet building codes but provide much higher levels of security than the standard door pull handle.

## Slide 17: Fire Security and Safety
Most serious threat to safety of people who work in an organization is possibility of fire
Fires account for more property damage, personal injury, and death than any other threat
Imperative that physical security plans examine and implement strong measures to detect and respond to fires
Notes: Fire Safety
The most serious threat to physical security and the safety of the people who work in the organization is the possibility of fire.
Fires account for more property damage, personal injury, and death than any other threat to physical security.
As a result, it is imperative that physical security plans examine and implement strong measures to detect and respond to fires and fire hazards.

## Slide 18: Fire Detection and Response
Fire suppression systems: devices installed and maintained to detect and respond to a fire
Flame point: temperature of ignition
Deny an environment of heat, fuel, or oxygen
  Water and water mist systems
  Carbon dioxide systems
  Soda acid systems
  Gas-based systems
Notes: Fire Detection and Response
Fire suppression systems are devices installed and maintained to detect and respond to a fire, potential fire, or combustion situation.
These devices typically work to deny an environment of one of the three requirements for a fire to burn: temperature, fuel, and oxygen.
Water and water mist systems reduce the temperature of the flame to extinguish it and to saturate some categories of fuels to prevent ignition.
Carbon dioxide systems rob fire of its oxygen.
Soda acid systems deny fire its fuel, preventing spreading.
Gas-based systems disrupt the fire’s chemical reaction but leave enough oxygen for people to survive for a short time.

## Slide 19: Fire Detection and Response (cont’d.)
Fire detection
  Fire detection systems fall into two general categories: manual and automatic
  Part of a complete fire safety program includes individuals that monitor chaos of fire evacuation to prevent an attacker accessing offices
  There are three basic types of fire detection systems: thermal detection, smoke detection, flame detection
Notes: Fire Detection
Before a fire can be suppressed, it must be detected.
Fire detection systems fall into two general categories: manual and automatic.
Manual fire detection systems include human responses, such as calling the fire department, as well as manually activated alarms, such as sprinklers and gaseous systems.
During the chaos of a fire evacuation, an attacker can easily slip into offices and obtain sensitive information. As part of a complete fire safety program, it is advisable to designate individuals as floor monitors.
There are three basic types of fire detection systems: thermal detection, smoke detection, and flame detection.
The thermal detection systems contain a sophisticated heat sensor that operates in one of two ways: fixed temperature and rate-of-rise.
Smoke-detection systems are perhaps the most common means of detecting a potentially dangerous fire and are required by building codes.
Smoke detectors operate in one of three ways:
1) Photoelectric sensors project and detect an infrared beam, which if interrupted activates alarm or suppression systems.
2) Ionization sensors contain a small amount of a harmless radioactive material within a detection chamber. When certain by-products of combustion enter, a change in the level of electrical conductivity activates the detector.
3) Air-aspirating detectors take in air, filtering it and moving it through a chamber containing a laser beam. If the laser beam is diverted or refracted by smoke particles, the system is activated.
The flame detector is a sensor that detects the infrared or ultraviolet light produced by an open flame.
These systems require direct line-of-sight with the flame and compare the flame “signature” to a database to determine whether or not to activate the alarm and suppression systems.
While highly sensitive, flame detection systems are expensive and must be installed where they can scan all areas of the protected area.

## Slide 20: Fire Detection and Response (cont’d.)
Fire suppression
  Systems consist of portable, manual, or automatic apparatus
  Portable extinguishers are rated by the type of fire: Class A, Class B, Class C, Class D
  Installed systems apply suppressive agents; usually either sprinkler or gaseous systems
Notes: Fire Suppression
Fire suppression systems can consist of portable, manual, or automatic apparatus. Portable extinguishers are rated by the type of fire:
Class A: Fires of ordinary combustible fuels. Use water and multipurpose, dry chemical fire extinguishers.
Class B: Fires fueled by combustible liquids or gases, such as solvents, gasoline, paint, lacquer, and oil. Use carbon dioxide, multipurpose dry chemical, and halon fire extinguishers.
Class C: Fires with energized electrical equipment or appliances. Use carbon dioxide, multi-purpose dry chemical, and halon fire extinguishers.
Class D: Fires fueled by combustible metals, such as magnesium, lithium, and sodium. Use special extinguishing agents and techniques.
Manual and automatic fire response can include installed systems designed to apply suppressive agents. These are usually either sprinkler or gaseous systems.
All sprinkler systems are designed to apply liquid, usually water, to all areas in which a fire has been detected.
In sprinkler systems, the organization can implement wet-pipe, dry-pipe, or pre-action systems.
Water mist sprinklers are the newest form of sprinkler systems and rely on ultra fine mists instead of traditional shower-type systems.

## Slide 21
Figure 9-3 Water sprinkler system

## Slide 22: Fire Detection and Response (cont’d.)
Gaseous emission systems
  Until recently, two types of systems: carbon dioxide and Halon
  Carbon dioxide robs a fire of oxygen supply
  Halon is clean but has been classified as an ozone-depleting substance; new installations are prohibited
  Alternative clean agents include FM-200, Inergen, carbon dioxide, FE-13 (trifluromethane)
Notes: Gaseous Emission Systems
Chemical gas systems can be used in the suppression of fires.
Until recently there were only two major types of gaseous systems: carbon dioxide and halon.
Carbon dioxide robs a fire of its oxygen supply.
Halon is a clean agent, which means that it does not leave any residue when dry, nor does it interfere with the operation of electrical or electronic equipment. Unfortunately the EPA has classified halon as an ozone-depleting substance, and therefore new installations are prohibited.
Alternative clean agents include the following:
FM-200
Inergen
Carbon dioxide
FE-13 (trifluromethane)

## Slide 23
Figure 9-4 Gaseous fire suppression system

## Slide 24: Failure of Supporting Utilities and Structural Collapse
Supporting utilities (heating, ventilation, and air conditioning; power; water; and others) have significant impact on continued safe operation of a facility
Each utility must be properly managed to prevent potential damage to information and information systems
Notes: Failure of Supporting Utilities and Structural Collapse
Supporting utilities, such as heating, ventilation, and air conditioning; power; water; and other utilities, have a significant impact on the continued safe operation of a facility.
Extreme temperatures and humidity levels, electrical fluctuations, and the interruption of water, sewage, and garbage services can create conditions that inject vulnerabilities in systems designed to protect information.

## Slide 25: Heating, Ventilation, and Air Conditioning
Areas within heating, ventilation, and air conditioning (HVAC) systems that can cause damage to information systems include:
  Temperature
  Filtration
  Humidity
  Static electricity
Notes: Heating, Ventilation, and Air Conditioning
Although traditionally a facilities management responsibility, the operation of the heating, ventilation, and air conditioning (HVAC) system can have dramatic impact on information and information systems operations and protection.
Specifically there are four areas within the HVAC system that can cause damage to information-carrying systems: temperature, filtration, humidity, and static electricity.
Temperature
  Computer systems are electronic and as such are subject to damage from extreme temperature.
  Rapid changes in temperature, from hot to cold, or from cold to hot can produce condensation, which can create short circuits or otherwise damage systems and components.
  The optimal temperature for a computing environment (and people) is between 70 and 74 degrees Fahrenheit.
Humidity
  Humidity is the amount of moisture in the air.
  High humidity levels create condensation problems, and low humidity levels can increase the amount of static electricity in the environment.
  With condensation comes the short-circuiting of electrical equipment and the potential for mold and rot in paper-based information storage.
Static
  Static electricity is caused by a process called triboelectrification, which occurs when two materials are rubbed or touched and electrons are exchanged, resulting in one object becoming more positively changed and the other more negatively charged.
  When a third object with an opposite charge or ground is encountered, electrons flow again and a spark is produced.
  One of the leading causes of damage to sensitive circuitry is electro-static discharge (ESD).
Static
  Integrated circuits in a computer use between two and five volts of electricity.
  Voltage levels as low as 200 can cause microchip damage.
  Static electricity is not even noticeable to humans until levels approach 1,500 volts, and you can’t see the little blue spark until it approaches 4,000 volts.
  A person can generate up to 12,000 volts of static current by walking across a carpet.
Static
  Two types of failures can result from ESD damage to chips. Immediate failures, also known as catastrophic failures, occur right away and are usually totally destructive.
  Latent failures or delayed failures can occur weeks or even months after the damage is done.
  It is imperative to maintain the optimal level of humidity, which is between 40 and 60 percent in the computing environment. Humidity levels below this range create static, and levels above create condensation.

## Slide 26: Heating, Ventilation, and Air Conditioning (cont’d.)
Ventilation shafts
  While ductwork is small in residential buildings, in large commercial buildings it can be large enough for an individual to climb though
  If vents are large, security can install wire mesh grids at various points to compartmentalize the runs
Notes: Ventilation Shafts
One last discussion point within the topic of HVAC is the security of the ventilation system air ductwork.
While in residential buildings the ductwork is quite small, in large commercial buildings it can be large enough for an individual to climb though.
If the vents are large, security can install wire mesh grids at various points to compartmentalize the runs. In any case, the ventilation system is one more area within the HVAC that must be evaluated.

## Slide 27: Heating, Ventilation, and Air Conditioning (cont’d.)
Power management and conditioning
  Electrical quantity (voltage level, amperage rating) and quality of power (cleanliness, proper installation) are concerns
  Noise that interferes with the normal 60 Hertz cycle can result in inaccurate time clocks or unreliable internal clocks inside CPU
Notes: Power Management and Conditioning
Not only is electrical quantity (voltage level and amperage rating) of concern, but so is the quality of the power (cleanliness and proper installation).
Interference with the normal pattern of the electrical current is referred to as noise in the current.
Any noise that interferes with the normal 60 Hertz cycle can result in inaccurate time clocks or, even worse, unreliable internal clocks inside the CPU.
Grounding
  Grounding ensures that the returning flow of current is properly discharged to the ground.
  If this is not properly installed, anyone touching a computer or other electrical device could be used as a ground source, causing damage to equipment and injury or death to the person.
  Power should also be provided in sufficient amperage to support needed operations.
  Overloading a circuit not only causes problems with the circuit tripping but can also overload the power load on an electrical cable, creating the risk of fire.

## Slide 28: Heating, Ventilation, and Air Conditioning (cont’d.)
Grounding and amperage
  Grounding ensures that returning flow of current is properly discharged to ground
  Overloading a circuit causes problems with circuit tripping and can overload electrical cable, increasing risk of fire
  GFCI: capable of quickly identifying and interrupting a ground fault
Notes: Uninterruptible Power Supplies (UPSs)
In case of power outage, a UPS is a backup power source for major computer systems.
There are four basic configurations of UPS:
The standby
Ferroresonant standby
Line-interactive
The true online
A standby or offline UPS is an offline battery backup that detects the interruption of power to the power equipment.
A ferroresonant standby UPS is still an offline UPS; the ferroresonant transformer reduces power problems.
The line-interactive UPS is always connected to the output, so it has a much faster response time and incorporates power conditioning and line filtering
The true online UPS works in the opposite fashion of a standby UPS since the primary power source is the battery, with the power feed from the utility constantly recharging the batteries. This model allows constant feed to the system, while completely eliminating power quality problems.

## Slide 29: Heating, Ventilation, and Air Conditioning (cont’d.)
Uninterruptible power supply (UPS)
  In case of power outage, UPS is backup power source for major computer systems
  Four basic UPS configurations:
    Standby
    Ferroresonant standby
    Line-interactive
    True online (double conversion online)

## Slide 30
Figure 9-5 Types of uninterruptible power supplies9
Source: Courtesy of American Power Conversion Corporation

## Slide 32: Heating, Ventilation, and Air Conditioning (cont’d.)
Emergency shutoff
  Important aspect of power management is the need to be able to stop power immediately should a current represent a risk to human or machine safety
  Most computer rooms and wiring closets are equipped with an emergency power shutoff
Notes: Emergency Shutoff
One important aspect of power management in any environment is the need to be able to stop power immediately should the current represent a risk to human or machine safety.
Most computer rooms and wiring closets are equipped with an emergency power shutoff, which is usually a large red button prominently placed to facilitate access, with an accident-proof cover to prevent unintentional use.

## Slide 33: Water Problems
Lack of water poses problem to systems, including functionality of fire suppression systems and ability of water chillers to provide air-conditioning
Surplus of water, or water pressure, poses a real threat (flooding, leaks)
Very important to integrate water detection systems into alarm systems that regulate overall facilities operations
Notes: Water Problems
Lack of water poses problem to systems, including the functionality of fire suppression systems and the ability of water chillers to provide air-conditioning.
On the other hand, a surplus of water or water pressure poses a real threat.
It is therefore important to integrate water detection systems into the alarm systems that regulate overall facilities operations.

## Slide 34: Structural Collapse
Unavoidable forces can cause failures of structures that house organization
Structures designed and constructed with specific load limits; overloading these limits results in structural failure and potential injury or loss of life
Periodic inspections by qualified civil engineers assist in identifying potentially dangerous structural conditions
Notes: Structural Collapse
Unavoidable environmental factors or forces of nature can cause failures of structures that house the organization.
Structures are designed and constructed with specific load limits, and overloading these design limits, intentionally or unintentionally, inevitably results in structural failure and potentially loss of life or injury.
Periodic inspections by qualified civil engineers assist in identifying potentially dangerous structural conditions well before they fail.

## Slide 35: Maintenance of Facility Systems
Physical security must be constantly documented, evaluated, and tested
Documentation of facility’s configuration, operation, and function should be integrated into disaster recovery plans and operating procedures
Testing helps improve the facility’s physical security and identify weak points
Notes: Testing Facility Systems
Just as with any phase of the security process, the physical security of the facility must be constantly documented, evaluated, and tested.
Documentation of the facilities configuration, operation, and function is integrated into disaster recovery plans and standing operating procedures.
Testing provides information necessary to improve the physical security in the facility and identifies the area’s weak points.

## Slide 36: Interception of Data
Three methods of data interception:
  Direct observation
  Interception of data transmission
  Electromagnetic interception
U.S. government developed TEMPEST program to reduce risk of electromagnetic radiation (EMR) monitoring
Notes: Interception of Data
There are three methods of data interception: direct observation, interception of data transmission, and electromagnetic interception.
With direct observation, one must be close enough to information to breach confidentiality. Physical security mechanisms can restrict the possibility of an individual accessing unauthorized areas and thus directly observing information.
On the other hand, if attackers can access the transmission media, i.e., by using the Internet or tapping the LAN, they need not be anywhere near the source of information.
It is possible to eavesdrop on signals from cables that emit electro-magnetic signals without actually tapping into them. TEMPEST is a technology that involves the monitoring of devices that emit electromagnetic radiation (EMR) in such a manner that the data can be reconstructed.
TEMPEST monitoring involves the following: ensuring that computers are placed as far as possible from outside perimeters; installing special shielding inside the CPU case; and implementing a host of other restrictions, including maintaining distances from plumbing and other infrastructure components that carry radio waves.

## Slide 37: Mobile and Portable Systems
With the increased threat to information security for laptops, handhelds, and PDAs, mobile computing requires more security than average in-house system
Many mobile computing systems
  Have corporate information stored within them
  Some are configured to facilitate user’s access into organization’s secure computing facilities
Notes: Mobile and Portable Systems
With the increased threat to overall information security for laptops, handhelds, and PDAs, mobile computing requires even more security than the average in-house system.
Many of these mobile computing systems not only have corporate information stored within them, but many are configured to facilitate the user’s access into the organization’s secure computing facilities.

## Slide 38: Mobile and Portable Systems (continued)
Controls support security and retrieval of lost or stolen laptops
  CompuTrace software, stored on laptop; reports to a central monitoring center
  Burglar alarms made up of a PC card that contains a motion detector
Notes: Mobile and Portable Systems (continued)
New technology to support the location of lost or stolen laptops can provide additional security.
The first type of new technology is CompuTrace, computer software that is stored on a laptop’s hardware and reports itself and the electronic serial number of the computer on which it is installed to a central monitoring center.
Also available for laptops are burglar alarms made up of a PC card that contains a motion detector.
If the alarm in the laptop is armed and the laptop is moved beyond a configured distance, the alarm triggers an audible alarm.
The system also shuts down the computer and includes an encryption option to completely render the information unusable.
For maximum security, laptops should be secured at all times.
If you are traveling with a laptop, you should have it in your possession at all times.

## Slide 39
Figure 9-6 Laptop theft deterrence

## Slide 40: Remote Computing Security
Remote site computing: away from organizational facility
Telecommuting: computing using telecommunications including Internet, dial-up, or leased point-to-point links
Employees may need to access networks on business trips; telecommuters need access from home systems or satellite offices
To provide secure extension of organization’s internal networks, all external connections and systems must be secured
Notes: Remote Computing Security
Remote site computing includes a wide variety of computing sites, which are distant from the base organizational facility and include the entire spectrum of telecommuters (or telecomputers).
Telecommuting involves computing using telecommunications facilities including Internet, dial-up, or leased point-to-point links.
Employees may need to access home networks on business trips, telecommuters need access from home systems, and some organizations even have satellite offices that need to be tightly integrated into the overall IT infrastructure.
Individuals telecommuting from home deserve special attention. As more individuals consider telecommuting, the risk to organizational information through these often unsecured connections is substantial.
Few organizations provide their employees with secure connections to their office networks, and even fewer provide secure systems, should the employee’s home computer be compromised.
To provide a secure extension of the organization’s internal networks, all external connections and systems must be secured.
Although it is possible to secure remote sites, organizations cannot assume the employees invest their own funds for security.

## Slide 41: Special Considerations for Physical Security Threats
Develop physical security in-house or outsource?
  Many qualified and professional agencies
  Benefit of outsourcing includes gaining experience and knowledge of agencies
  Downside includes high expense, loss of control over individual components, and level of trust that must be placed in another company
Social engineering: use of people skills to obtain information from employees that should not be released
Notes: Special Considerations for Physical Security Threats
There are a number of special considerations for physical security threats that should be examined.
The first of these is the decision to develop physical security in-house or to outsource it.
There are a number of qualified and professional agencies that provide consulting and services in the physical security area.
The benefit of outsourcing physical security includes gaining the experience and knowledge of these agencies, many of which have been in the field for decades.
The downside includes the high expense of outsourcing physical security, the loss of control over the individual components of the physical security solution, and the level of trust that must be placed in another company.
Another area of physical security deals with social engineering.
Social engineering is the use of people skills to obtain information from employees without their knowing it.
While most social engineers prefer to use the telephone and computer to make their contacts and solicit information, there are those who are brazen in accessing the information more directly.
Require all individuals entering the facility to display appropriate visitor’s badges and be escorted by a security individual when in restricted areas.

## Slide 42: Inventory Management
Computing equipment should be inventoried and inspected on a regular basis
Classified information should also be inventoried and managed
Physical security of computing equipment, data storage media, and classified documents varies for each organization
Notes: Inventory Management
As with other organizational resources, computing equipment should be inventoried and inspected on a regular basis. Similarly classified information should also be inventoried and managed.
Whenever a classified document is reproduced, a stamp should be placed on the original before it is copied.
This stamp states the document’s classification level and document number for tracking.
Each classified copy is issued to its receiver, who signs for the document.

## Slide 43: Summary
Threats to information security that are unique to physical security
Key physical security considerations in a facility site
Physical security monitoring components
Essential elements of access control
Fire safety, fire detection, and response
Importance of supporting utilities, especially use of uninterruptible power supplies
Countermeasures to physical theft of computing devices